## Slide 1: Remote Measurement and monitoring
Wesley Myers

## Slide 2: Project Goals
Remote Measurement
Web Interface Control
Remote Viewing
Autonomy for Monitoring
Requirement Driver

## Slide 3: Requirements
Measure distance (+/- 1 cm) to targets out to 50 meters
View Targets with Camera
Remote/automated pan-tilt system
Wireless Control
Control through Web Interface

## Slide 4: System Layout
Raspberry Pi
Webserver
Range Finder
Pan Servo
Tilt Servo
GPIO
CSI
Bus
Raspberry Pi Camera
OpenCV
WiFi Dongle
USB

## Slide 5: Equipment
Item | Qty | Cost
Raspberry Pi | 1 | $40.00
Camera | 1 | $35.00
Camera (IR) | 1 | $35.00
Laser Range Finder | 1 | $500.00
Wifi Dongle | 1 | $12.00
Servos | 2 | $10.00
Other Materials |  | unknown

## Slide 6
Laser Range Finder
http://www.lightware.co.za/shop/en/lrf-modules/31-sf01a.html
Industrial Grade Laser Range Finders
Interface-able with Raspberry Pi
850 nm Wavelength

## Slide 7
Camera / OpenCV
2592 x 1499 pixels
NoIR Camera Board
Automatic Feature Detection
Notes: LPF
R = 1 kOhm
C = 15 micro Farads

## Slide 8: Challenges
.02 m
50 m
.23 degrees
Use of Servos
Detection of small targets

## Slide 9
FSM Overview
User Selects Target to Measure within FOV
Aim Pan-Tilt Towards Target
Aimed?
Execute Measurement Algorithm
Display Information to User
Yes
No
Notes: LPF
R = 1 kOhm
C = 15 micro Farads

## Slide 10: Algorithm
TL-TR
TR-BR
BR-BL
BL-TL
TL-BR
BL-TR
1-degree
1-degree
TL
TR
BR
BL
Pan-Tilt over available area
Combination of inputs

## Slide 11: Verification Testing
Questions
  Can we see the laser?
Notes
  Kinect outputs 830 nm wavelength
Results
  Not visible in daylight
  Sporadic
  Inconclusive
Future Testing
  Test with IR Camera

## Slide 12: Schedule
Date | Milestone
September 29th | Ordering and Receiving Equipment
October 6th | Pan Tilt Mechanism / CDR Due / TDY Tuesday – Friday
October 13th | Camera and Laser Integration
October 20th | Continue Integration / TDY Sunday - Wednesday
October 27th | OpenCV Development
November 3rd | UI and Webserver Design
November 10th | Algorithm Development
November 17th | Algorithm Development
November 24th | Testing and Analysis
December 1st | Testing and Analysis
December 8th | Project Documentation Due
December 13th | Final Presentation

## Slide 13: Reach Goals
Addition of Security Camera Features
  Automatic Motion Detection
  Email/Text Alert
  Saving imagery to Dropbox

## Slide 14: Questions?